Applications

The American-Marsh model HH multistage splitcase pumps are designed for long, dependable life in many applications.  The model HH multistage splitcase pumps operate at 3500 RPM quietly and efficiency.  The HH product line, with its many options, allows the end user increased flexibility in todays pump applications.

PRODUCT BULLETIN

MODEL HH MULTISTAGE HSC

Material Specifications

| PART | CONSTRUCTION |
| --- | --- |
|  | BRONZE FITTED | ALL IRON | NI-RESIST FITTED | 316SS FITTED |
| Casing | Cast Iron | Cast Iron | Cast Iron | Cast Iron |
| Impellers | Bronze | Cast Iron | Ni-Resist | 316 Stainless Steel |
| Shaft | 420 Stainless Steel | 420 Stainless Steel | 420 Stainless Steel | 420 Stainless Steel |
| Lantern Rings | Bronze | Cast Iron | Ni-Resist | 316 Stainless Steel |
| Stuffing Box Glands | Bronze | Cast Iron | Ni-Resist | 316 Stainless Steel |
| Shaft Sleeves | Bronze | Stainless | Stainless | 316 Stainless Steel |
| Bearing Housings | Cast Iron | Cast Iron | Cast Iron | Cast Iron |
| Mechanical Seal | Carbon/Si-C/Buna | Carbon/Si-C/Buna | Carbon/Si-C/Buna | Carbon/Si-C/Buna |

MODEL HH SPECIFICATIONS

Casing:  The casing is of high tensile cast iron or other specified material.  It is of the volute type, split on the horizontal center line with the suction and discharge flanges as well as the bearing brackets cast integral with the lower half. Removal of the upper half of the casing gives complete access to the interior of the pump without disturbing the piping connections or pump alignment.

Impellers:  The impellers are of the single suction, enclosed, non-overloading type.  They are placed back to back to balance the end thrust without the use of extra seal rings or other balancing devices.   Impellers are made of high tensile cast iron, or other special material, machined and polished all over, and dynamically and hydraulically balanced.  They are keyed to the shaft, secured by lock nuts and adjustable for position.

Case Wear Rings:  Case wear rings are made of high tensile cast iron or other specified material.  They are of the labyrinth type with the diameter at wearing surface reduced to a minimum, and are firmly secured in the casing by dowel pins.

Shaft:  The shaft is of 420 stainless steel, ground to accurate dimensions and polished to a smooth surface.  It is designed for extra stiffness to avoid all critical speeds in operation, and is threaded for bearing and lock nuts.

Shaft Sleeves:  are of bronze, or other specified material, extending from the impeller hub through the stuffing boxes and secured to the shaft by twin positive locknuts.  Stuffing boxes prevent leakage along the shaft while allowing freedom for the sleeve to expand independently of the shaft expansion.

Stuffing Boxes:  The stuffing boxes are extra deep, designed for six rings of packing in addition to the lantern ring.  Under each stuffing box is a drip pocket with tapped drain outlet.  A wide variety of mechanical seals are available upon request.

Glands:  The glands are of the hinge bolt type, split for easy removal and fastened together with capscrews.

Bearings:  Both the inboard and outboard ball bearings are of the single row, deep groove type, precision grade, with cartridge mounting, permitting the removal of the shaft without exposing or disturbing the bearing assembly.  They are of extra large capacity for both radial and thrust loads, and are locked to the shaft with nut and positive nut lock.  The outboard bearing is confined rigidly in the bearing housing to take the end thrust, while the inboard bearing is set with sufficient clearance to allow for shaft expansion.  Each bearing is designed for grease lubrication and is provided with a water slinger to prevent leakage from the stuffing box into the bearing.  A grease zerk fitting is furnished for each bearing.

HH Sectional Drawing

| Item Number | Item Description | Num. Req. |  | Item Number | Item Description | Num. Req. |
| --- | --- | --- | --- | --- | --- | --- |
| 1A | Casing | 1 |  | 85N | Cap, Housing, Outboard | 1 |
| 11H | Impeller, 1st Stage | 1 |  | 85P | Cap, Housing, Inboard | 1 |
| 11J | Impeller, 2nd Stage | 1 |  | 87N | Spacer, Bearing | 1 |
| 15A | Ring, Casing Wearing | 2 |  | 87P* | Spacer, Bearing | 1 |
| 16A | Pin, Dowel, Casing Ring | 2 |  | 88M | Ring, Oil | 2 |
| 16B | Pin, Dowel, Casing Bushing | 1 |  | 86M | Strap, Housing | 2 |
| 18B | Bushing, Casing | 1 |  | 89N | Locknut, Bearing, Outboard | 1 |
| 24A | Key, Impeller | 1 |  | 89P | Locknut, Bearing, Inboard | 1 |
| 41D | Shaft | 1 |  | 91N | Lockwasher, Bearing, Outboard | 1 |
| 42B | Sleeve, Shaft, RH | 1 |  | 91P | Lockwasher, Bearing, Inboard | 1 |
| 42C | Sleeve, Shaft, LH | 1 |  | 93N | Pin, Housing Thrust, Outboard | 1 |
| 43B | Shaft Sleeve Nut, RH | 1 |  | 93P | Pin, Housing Thrust, Inboard | 1 |
| 43C | Shaft Sleeve Nut, LH | 1 |  | 97N | Bearing Cap, Outbd/Inbd | 1 |
| 45A | Bushing, Shaft | 2 |  | 97P | Bearing Cap, Inbd/Inbd | 1 |
| 71A | Gland, Complete | 2 |  | 281A | Fitting, Zerk | 2 |
| 72B | Bolt, Gland, with Nut and Washer | 4 |  | 331A | Packing, Stuffing Box | 1 set |
| 73A | Ring, Lantern | 1 |  | 384C* | Screw, Bearing Cap | 8 |
| 81N | Bearing, Ball, Outboard | 1 |  | 411A | Plug, Pipe, Vent | 2 |
| 81P | Bearing, Ball, Inboard | 1 |  | 411D | Plug, Pipe, Bearing Cap | 1 |
| 82N | Housing, Bearing, Outboard | 1 |  | 353A* | Gasket, Casing | 1 |
| 82P | Housing, Bearing, Inboard | 1 |  | 381B* | Bolt, Casing | Varies |

* Not shown in sectional.

Recommended spare parts are in BOLD.

# Text boxes

PRODUCT BULLETIN			MUNICIPAL				COMMERCIAL			INDUSTRIAL

MODEL HH MULTISTAGE		Booster Systems, Chemical Injection	HVAC, Booster, Boiler Feed,		Process, Petrochemical,

High Rise, Condenser Water		Chemical Injection

Bulletin 380HH

Edition 4d

Bulletin 380HH

Edition 4d