The American-Marsh model HT horizontal multistage turbine pumps are designed for long, dependable life in many applications.  The Model HT multistage turbine pumps operate at 3500 RPM quietly and efficiency.  Due to the unique design, the single mechanical seal is only under suction pressure, extending seal life and reducing cost.  The HT product line, with its many options, allows the end user pincreased flexibility in todays pump applications.

PRODUCT BULLETIN

MODEL HT MULTISTAGE TURBINE

Material Specifications

| PART | CONSTRUCTION |
| --- | --- |
|  | BRONZE FITTED | ALL IRON | NI-RESIST FITTED | 316SS FITTED |
| Bowl Assembly | Cast Iron | Cast Iron | Cast Iron | Cast Iron |
| Suction Head | Fabricated Steel | Fabricated Steel | Fabricated Steel | Fabricated Steel |
| Bearing Stage | Cast Iron | Cast Iron | Cast Iron | Cast Iron |
| Thrust Bearing Hsg. | Cast Iron | Cast Iron | Cast Iron | Cast Iron |
| Impellers | Bronze | Cast Iron | Ni-Resist | 316 Stainless Steel |
| Shaft | 416 Stainless Steel | 416 Stainless Steel | 316 Stainless Steel | 316 Stainless Steel |
| Bearing Housings | Cast Iron | Cast Iron | Cast Iron | Cast Iron |
| Mechanical Seal | Carbon/Si-C/Buna | Carbon/Si-C/Buna | Carbon/Si-C/Buna | Carbon/Si-C/Buna |

MODEL HT SPECIFICATIONS

Bowl Assembly:  The pump bowls shall be of close grained, cast iron ASTM A48 Class 30.  The water passages shall be lined with porcelain enamel, shall be free of blow holes, sand holes and other detrimental defects, and shall be accurately machined and fitted.  The impellers are of the single suction, enclosed, francis, non-overloading type and are dynamically balanced.  Impellers shall be securly fastened to the shaft with taper split bushings of steel.  Upon request, impellers can be keyed to the shaft.  Impellers shall be adjusted vertically by an external means.

The pump shaft shall be of A582 grade 416 stainless steel, turned, ground and polished.  It shall be supported by bronze bearings on both sides of each impeller.  The size of the shaft shall be no less than that determined by ANSI/AWWA Specifications E101, Section A4.3 paragraph 4.3.3.

Suction Head:  The suction head shall be of Schedule 40 fabricated steel, free from defects, accurately machined and with a surface discharge.  The suction flange shall be machined and drilled to ANSI standards for 125 pounds rating.  The driver side of the suction head shall have a rabbet fit to accurately locate the c-face driver

The standard cast iron seal chamber shall be rated for 125 PSI discharge pressure and shall be fitted with an American-Marsh 810 series low pressure mechanical seal.  The seal chamber  housing is bolted to the head with an o-ring seal.  Seal materials shall be compatible with the liquid pumped.  Optional mechanical seals are available upon request.

Thrust Bearing Housing:  The thrust bearing shall be chosen to handle the continuous axial thrust as specified by the pump manufacturer with an AFBMA B-10 one-year minimum or five year average life under design conditions.  Provisions shall be made for momentary upthrust equal to 30 percent of rated down thrust.  The thrust bearing shall have provisions for adjusting the lateral clearances of the pump and should be sealed with a lip seal to keep out contaminents.

Motor:  The electric motor shall be c-face, 3500 RPM., three phase (50 or 60 Hz) squirrel cage induction design.  Enclosure shall be TEFC or other specified type.  Motor shall have Class B or Class F insulation with temperature rise as specified by NEMA standards for class insulation used and shall have a 1.15 service factor.

HT Sectional Drawing

| Item Number | Item Description | Num. Req. |  | Item Number | Item Description | Num. Req. |
| --- | --- | --- | --- | --- | --- | --- |
| 1A | Bowl Assembly | Varies |  | 47A | Set Screw, Bearing Adapter | 2 |
| 1B | Seal Chamber | 1 |  | 81S | Bearing, Thrust | 1 |
| 1C | Motor Bracket | 1 |  | 82S | Housing, Bearing | 1 |
| 1D | Suction Head | 1 |  | 85S | Cap, Thrust Bearing | 1 |
| 1E | Discharge Flange | 1 |  | 89S | Locknut | 1 |
| 2 | Bearing Stage | 1 |  | 89N | Lockwasher | 1 |
| 11T | Impeller | Varies |  | 92S | Adapter, Thrust Bearing | 1 |
| 41 | Shaft | 1 |  | 100N | Lip Seal, Bearing Housing | 1 |
| 42T | Impeller Collet | Varies |  | 331B | Mechanical Seal | 1 |
| 45R | Bearing, Seal Chamber | 1 |  | 450 | Coupling, Motor | 1 |
| 45S | Bearing, Bearing Stage | 1 |  | 500 | Motor | 1 |
| 45T | Bearing, Bowl | Varies |  |  |  |  |

Recommended spare parts are in BOLD.

# Text boxes

PRODUCT BULLETIN			MUNICIPAL				COMMERCIAL			INDUSTRIAL

MODEL HT MULTISTAGE		Booster Systems, Chemical Injection	HVAC, Booster, Boiler Feed,		Process, Petrochemical,

High Rise, Condenser Water		Chemical Injection

Bulletin 380HT

Edition 2

Bulletin 380HT

Edition 2